River-routing in CCAM

---
Method used for river-routing
Calculate slope,
i
Calculate velocity:
u = 0.35 sqrt{i/i_0}
Calculate nett mass flow
[kg/m^2]
Read “Water level” [kg/m^2]
Read Topography [m]
Update water levels

---
Trapped water removal
- Trapped water if water inflow from all sides
- Water removed by adding it to soil moisture
- Other modes will store water or leak it into soil at all grid points and not just for basins

---
Model specs
- C48 grid 48*48*6 = 13 824 cells
- Quasi-uniform resolution of:
  - i.e.
- Initially, no water: C-CAM spins up rivers as it runs
  - Rain, ice-melt
- Saves a water-body variable so it can be initialised from new values
- Water-body output is given as surface water in the variable, swater
%delta x equiv %delta y = 2%pi R/( 4N)
%delta x equiv %delta y = 208 km

---
Simulation results: Year 2000
Not spinned-up just yet

---
Simulation results continued: Water levels

---
What we're using currently:
- Python: numpy, netCDF4's Dataset, matplotlib, mpl_toolkits (Basemap utility)
  - EASY and available on my github
- Version-control for scripts: git and github
- Storage of massive output files: Prayer.
  - Can we access your outputs via the CHPC? (Charles Crosby?)

---
Really (really) need the following
- Water-level data for Amazon
- Lat-lon coordinates with water-level over span of years.
- The more the better
  - Verification of C-CAM as is
  - Verification of river-routing once detached from C-CAM
  - Basis for machine learning training
- Run scripts (nriver = 1??)
- NetCDF output from your runs (with swater and runoff)
- Has anyone tried to compare the swater output with data yet? (CSIR, CSIRO??). Perhaps on higher resolution?

---
SCRIPTS
DATA